## Slide 1: RIFFA 2.2.2 for dummy
2018/04/09 v1.0 Sheng Jui Huang
2019/07/17 v2.0 Shih Wei Hsieh

## Slide 2: Outline
What is RIFFA
Practice #1
Practice #2
Appendix

## Slide 3: What is RIFFA
RIFFA:
  Reusable Integration Framework for FPGA Accelerators
  Requires a PCIe enabled workstation and a FPGA board with a PCIe connector
Pros:
  Both the software and hardware interfaces have been greatly simplified
  Ease of programming: details of the PCIe protocol, device driver, DMA operation, and all hardware addressing are hidden from both the software and hardware.
  Support for Linux and Windows, software bindings for C/C++, Python, Matlab, and Java
Cons:
  Takes up resource: If no high speed data I/O communication is needed, then its better to not use it
  Loss of flexibility

## Slide 4: What is RIFFA
User cores interface with RIFFA 2.0 via a Channel core
The Channel core has FIFOs for receiving and sending data respectively.
The RX Engine core is responsible for extracting and demultiplexing received PCIe payload data.
The TX Engine core is responsible for formatting payload data into PCIe packets and multiplexing access to the PCIe link
The PCIe link configuration determines the width of the data bus. This width can be 32, 64, or 128 bits wide (RIFFA does not support 256 bits interface)
All PCIe Gen 1 and Gen 2 configurations up to x8 lanes are supported.
Where you need to plug your design

## Slide 5: What is RIFFA
Sending data in smaller transfer sizes reduces effective throughput
Making a copy of a large buffer of data in software before sending it to the FPGA takes time and can severely impact throughput
Less transmission improves throughput

## Slide 6: Hardware Interface
RX/ TX protocol:
  Read: https://sites.google.com/a/eng.ucsd.edu/matt-jacobsen/riffa/riffa_2_0/hw-interface
  Learn from example: our sample code

## Slide 7: Software Interface
RX/ TX protocol:
  Read: https://sites.google.com/a/eng.ucsd.edu/matt-jacobsen/riffa/riffa_2_0/c-interface
  Learn from example: our sample code

## Slide 8: Recommended design tips
It is recommended that you separate your design from the RIFFA transmission part
Pros:
  Easier to maintain your code
  You can test your code using ncverilog simulation before programming it on FPGA
    Easier to debug your code
    Saves your time (Quartus compilation is time-consuming)
Your design
Testbench
pattern generator
RIFFA Channel
RIFFA software interface
ASIC flow
FPGA flow

## Slide 9: Practice time
More info (website/ paper/ github):
  https://sites.google.com/a/eng.ucsd.edu/matt-jacobsen/riffa/riffa_2_0
  http://kastner.ucsd.edu/wp-content/uploads/2014/04/admin/fpl-riffa2.pdf
  https://github.com/KastnerRG/riffa
DE4 workstation:
  IP: 140.112.48.159
  Port: 42020
Download:
  https://github.com/b03901165Shih/2019-FPGA-training-course
  cp –r /mnt/ds1515/fpga/riffa_2.2.2/ ./
Use this to copy riffa from our workstation

## Slide 10: Practice time
Practice #1: Block RAM
  Input Store in BRAM Read from BRAM (reverse order) Output
Block RAM
Data input
Data output

## Slide 11: Practice time
Channel tester:
Plugged design

## Slide 12: Practice time
Inferred dual port Block RAM:

## Slide 13: Step-by-step guide
Download sample code:
    https://github.com/b03901165Shih/2019-FPGA-training-course
Generate pattern from bram_wrapper.m (done)
Simulate with ncverilog
    IC design workstation: 140.112.48.159 port 41140
    Source file: source /cad/source.cshrc
    Simulate: ncverilog tb_bram.v bram_wrapper.v +access+r
Practice 1

## Slide 14: Step-by-step guide
Open Quartus II (License file: 25000@140.112.33.164)
  Quartus 15.0 (for DE4 projects):
    /mnt/ds1515/opt/intelFPGA/15.0/quartus/bin/quartus &
  Quartus 17.0:
    /mnt/ds1515/opt/intelFPGA/17.0/quartus/bin/quartus &
Copy RIFFA from workstation
    cp –r /mnt/ds1515/fpga/riffa_2.2.2/ ./
Open Project
  Located at:
    <your path>/riffa_2.2.2/source/fpga/altera/de#/DE#Gen#x#If###/prj/DE#Gen#x#lf###.qpf
    de#: de4/ de5
    DE#Gen#x#If###: DE4Gen2x8If128
      FPGA: DE4
      PCIe Spec: generation 2; 8 lanes; 128 bits width (250 MHz)
Gen2x8 | 250 MHz/ 128 bits
Gen2x4 | 125 MHz/ 128 bits

## Slide 15: Step-by-step guide
Replace files in RIFFA directory:
Compile:
(may take some time)
<your path>/riffa_2.2.2/source/fpga/riffa_hdl/
<your path>/riffa_2.2.2/source/c_c++/linux/x64/
Press
(Delete original sample_app)

## Slide 16: Step-by-step guide
Additional settings

## Slide 17: Step-by-step guide
Compilation report
Pay attention to these

## Slide 18: Step-by-step guide
Timing analyzer
  WNS should be positive for all corners
Not ok, but we’ll skip for now

## Slide 19: Step-by-step guide
Timequest timing analyzer
Critical path

## Slide 20: Step-by-step guide
Programmer
1.
2.
3.
4.
If “No hardware”:
sudo killall jtagd
sudo /mnt/ds1515/opt/intelFPGA/15.0/quartus/bin/jtagconfig
5. close

## Slide 21: Step-by-step guide
Reboot
    sudo reboot
Run
    cd <your path>/riffa_2.2.2/source/c_c++/linux/x64/sample_app
    make
    ./testutil 0 //List FPGA info
    ./testutil 1 0 //Reset FPGA 0
    ./testutil 2 <numofdata> //numofdata: multiples of 4 (up to 65536)
Congratulations !

## Slide 22: Practice time
Practice #2: Floating Point Unit
  Input Addition Store in BRAM Read from BRAM Output
Block RAM
Data input
Data output
(a, b, c, d)
(0, 0, 0, a+b+c+d)

## Slide 23: FPU IP
Library > Basic Functions > Arithmetic > ALTFP_ADD_SUB
  File name: FPU_add_sub.v
Choose 8 stages pipeline

## Slide 24: FPU IP
Library > Basic Functions > Arithmetic > ALTFP_ADD_SUB
  Next Next Next… Finish Yes

## Slide 25: TODOs
Finish alu_add in bram_wrapper.v at line 139
Simulation:
    ncverilog tb_bram.v bram_wrapper.v add.v +access+r
    Pass Next step

## Slide 26: TODOs
Follow the step-by-step guide to finish the FPGA part
Run:
  ./testutil 2 65536
If you see this, you passed the FPGA test
End of tutorial!

## Slide 27: Appendix: Modifying PCIe

## Slide 28: Modifying the PCIE
GEN
  1/2/3
LANE
  x1/x2/x4/x8/x16
62.5 MHz:
  Gen1x1
125 MHz:
  Gen1x2, Gen1x4
  Gen2x1, Gen2x2, Gen2x4, Gen2x8
  Gen3x1, Gen3x2
250 MHz:
  Gen2x8
  Gen3x4, Gen 3x8

## Slide 29: Modifying the PCIe on the Qsys
Double click on
  QSysDE#Gen#x#lf###:pcie_system_inst
Areas to be edited are highlighted
Edit settings in PCIeDE#Gen#x#lf### first
Then for XCVRCtrlGen#x#, and XDRVCtrlGen#x#
  Edit Number of reconfiguration interfaces accordingly

## Slide 30: Changing PCIe generation
Go to assignment editor
Change Values accordingly
  PCIE_GEN1
  PCIE_GEN2
  PCIE_GEN3

## Slide 31: Changing width
Go to DE#Gen#x#lf###.v
  Change parameter C_PCI_DATA_WIDTH to width
  For IP QSysDE#Gen#x#If### pcie_system_inst
    .rx_st_data (rx_st_data[C_PCI_DATA_WIDTH-1:0]),
    .tx_st_data (tx_st_data[C_PCI_DATA_WIDTH-1:0]),

## Slide 32: Changing number of lanes
Go to DE#Gen#x#lf###.v
  Change parameter C_NUM_LANES to number of lanes
  For IP QSysDE#Gen#x#If### pcie_system_inst
    .pcieserial_tx_out0 (PCIE_TX_OUT[0]),
    .pcieserial_tx_out1 (PCIE_TX_OUT[1]),
    ...
    .pcieserial_tx_out# (PCIE_TX_OUT[#]),
  AND
    .pcieserial_rx_in0 (PCIE_RX_IN[0]),
    .pcieserial_rx_in1 (PCIE_RX_IN[1]),
    ...
    .pcieserial_rx_in# (PCIE_RX_IN[#]),
      # = C_NUM_LANES - 1
Go to assignment editor
  Add PCIE_RX_IN[#], PCIE_RX_IN[#](n), PCIE_TX_OUT[#], PCIE_TX_OUT[#](n),